## Slide 1
The runMCXspectrum.m program can generate a reflectance spectrum over a chosen wavelength range.
This example generates R(nm) for nm = 300:10:1000.

## Slide 2
B = blood volume fraction
S = arteriovenous oxygen saturation
W = water content
M = melanosome volume fraction
C = dietary carotenoids
F = fat volume fraction
A = background absorption (constant over wavelength)
where X = C, M, F, …
where MU(:,:) is an array
that holds the absorption spectra for the tissue components
The basics of skin optical properties are summarized.
First, the absorption of a skin layer
containing different amounts of these
tissue components.

## Slide 3
a = scattering strength [1/mm]
b = scattering power
g = anisotropy of scatter
g
The basics of skin optical properties are summarized.
Second, the scattering properties
of a skin layer is specified.

## Slide 4
for tissue types #:
  1 = epidermis
  2 = papillary dermis
  3 = superficial vascular plexus
  4 = reticular dermis
The makeTissueList.m subroutine generates a tissue structure that holds the optical properties at one wavelength.

## Slide 5
The makeTissueList.m subroutine generates a tissue structure that holds the optical properties at one wavelength.

## Slide 6
% specify tissue layer properties
PRINTON=0;
tissue = makeTissueList_skinWorkshop(nm1, MU2(inm,:), PRINTON);
prop(1,:)=[0 0 1 1]; % outer boundary [mua mus g n]
for i=1:4 % epi pap plx ret
mua = tissue(i).mua + A;
mus = tissue(i).mus;
g = tissue(i).g;
n = tissue(i).n;
prop(i+1,:) = [mua mus g n];
end
prop(5+1,:) = [mua*1000 mus*1000 g n]; % mimic semi-infinite dermis
% 1=outer boundary
  % 2=epidermis
% 3=papillary dermis
% 4=vascular plexus
% 5=reticular dermis
% 6=semi-infinite dermis
cfg.prop = prop;
MCX uses makeTissueList.m
to fill the cfg.prop array that
specifies the optical properties
of each tissue layer.
A 6th tissue type is defined as dermis
with its absorption and scattering
increased 1000-fold.
The ratio of scattering/absorption
cancels the 1000 factor, so the
reflectance of this layer is the same
as the normal dermis.

## Slide 7
Fill the tissue volume with skin layers
Fill the tissue volume with the skin layers, including a final layer of 11-voxel thickness
Filled with the semi-infinite dermis properties (prop(6,:)) that mimics a semi-infinite dermis.
Models a semi-infinite tissue without requiring a ridiculously thick volume.
Alternatively, you might create
  finite-thickness dermis (eg., 2 mm),
  a sub-cutaneous vascular plexus,
  and a fat layer.
Note the semi-infinite mimic

## Slide 8
The lateral boundaries of the volume are set to “cyclic” so that no photons
are lost out the sides of the volume.
cfg.bc = 'ccrccr'; % cylic edges, reflective top,rear
The total reflectance is calculated by summing the Rxy array.
Rxy = flux.dref(:,:,1)*cfg.tstep*cfg.unitinmm^2;
R(inm,1) = sum( Rxy(:));
Hence, the resulting reflectance R is a 1D solution, i.e., the reflectance from an infinitely broad beam of incidence.

## Slide 9
Example: Run MCX using different amounts of epidermal melanin.
The melanosome volume fraction (M) in the epidermis is varied as 0, 2%, 6%.
This is accomplished by adjusting the value of M in makeTissueList.m:
tissue(1).name = 'epidermis';
M = 0.02; % melanosome volume fraction

## Slide 10
Example: Run MCX using different amounts of dietary carotenoids (C).
The factor C scales an experimental carotenoid absorption spectrum.
This is accomplished by adjusting the value CC in makeTissueList.m:
CC = 0.0; % Carotenoids (scales carotenoid absorption)
which then specifies the value tissue(#).C for all tissue types.
The carotenoids affect the 460-520 nm range.

## Slide 11
There is a background absorption (A [1/mm]) that should be included for skin.
In this example, A is a constant over all wavelengths, but primarily affects the longer wavelengths where photon pathlengths are long.
More work is needed on A, but a typical values is 0.01/mm.
Currently, the value of A is changed within the runMCXspectrum.m program, rather than within the makeTissueList.m subroutine,
because study of A is on-going. Eventually, A may be included in makeTissueList.m.

## Slide 12
A FINAL NOTE: Simulating the reflectance of a semi-infinite tissue as the ratio of N’=mus’/mua is varied.
This simulation used the semi-infinite mimic of cfg.prop(6,:) = [mua*1000 mus*1000 g n].
Comparison of the MCX R(N’) versus the diffusion theory R(N’) is shown.
For a matched surface boundary condition, the two calculations are indistinguishable on the R vs log(N’) plot.
For a mis-matched boundary condition, the MCX result deviates from the diffusion theory result when R<0.40.
When scattering no longer dominates absorption, the photons do not have enough scattering events
to become randomized before being absorbed. Hence, diffusion theory over-estimates reflectance.
Monte Carlo simulations are needed when the ratio N’ is less than 10.
The transmission (Tt) is zero.

## Slide 13
The same comparison of MCX vs Diffusion Theory on a log-log scale.
The curves illustrate that diffusion theory overestimates R(N’)
when N’<1 for a matched boundary, and
when N’<10 for a mismatched boundary.
For problems involving superficial scatter (confocal reflectance/fluorescence, OCT), Monte Carlo sims are needed.
For problems involving fluence around absorbing objects or near boundaries, Monte Carlo sims are needed.
Note: when N’ is very small,
there is still some transmission
despite the semi-infinite mimic.
Making the mimic more optically thick
could fix this transmission leakage.