## Slide 1: The 5th International MCX Training Workshop
Associate Professor
Dept. of Bioengineering
Northeastern University, USA
Qianqian Fang, PhD
MCX website: https://mcx.space
MCX’24, Northeastern University

## Slide 2: Outline
Group introduction
The MCX project
MC algorithm workflow highlights
Knowing the limits
Hardware recommendations

## Slide 3: Group Introduction
MCX website: https://mcx.space
MCX’24
Session 1.A

## Slide 4: MCX Training workshops
2017, 2019 at Northeastern Boston Campus
2018 at Hollywood, FL, OSA Biomedical Imaging
2022 at Boston fNIRS mini-course

## Slide 5: The MCX Project
MCX website: https://mcx.space
MCX’24
Session 1.B

## Slide 6: MCX Suite – full-stack solution
MCX
MCX-CL
MMC
(Trinity)
Iso2Mesh
Standalone
Mex files
MATLAB
GNU Octave
GUI
MCXLAB/CL
MMCLAB
MMC-SSE/CL/CUDA
MCX Cloud
Brain2mesh
pmcx

## Slide 7: Online resources
https://mcx.space
https://mcx.space/wiki/
https://mcx.space/cloud/

## Slide 8: Where MCX/MMC excel?
Speed
Accuracy
Tran AP+, Yan S+, Fang Q*, (2020) “Improving model-based fNIRS analysis using mesh-based anatomical and light-transport models," Neurophotonics, 7(1), 015008

## Slide 9: Acknowledgement
This project is funded by the NIH/NIGMS under the grant R01-GM114365 (MCX, https://mcx.space)
NIH/NINDS under grant U24-NS124027 (https://neurojson.org).
NIH/NCI under grant 2R01-CA204443.

## Slide 10: MCX Algorithm Highlights
MCX website: https://mcx.space
MCX’24
Session 1.C

## Slide 11: MCX/MMC Algorithm Diagram
Launch (p, v, w)
Determine unitless
scattering len. S
N photon?
End
Calculate the distance D to cell boundary, define d=min(D, S/µs)
Move photon by d: p= p+d*c
S=S-d*µs
Accumulate Δw to the cell enclosing the path
Cross a boundary & n1≠n2?
Arrive at a scattering site (S≤0)?
Do Reflection?
Reflect
Transmit
Determine new
Scattering dir: v
Time limit exceeds?
Exit domain?
n
y
y
n
n
y
y
n
n
y
y
n
Update packet weight Δw=w*[1-exp(-µad)]
w=w-Δw
Start

## Slide 12: Complex Source Types
Point sources:
  Pencil beam, isotropic source, cone beam
Line sources:
  Isotropic line source, slit source
Area sources:
  Planar, disk, Fourier domain source, Gaussian source, arbitrary 2D pattern source (load a 2D array)
All area/line sources support convergent and divergent beams (cfg.srcdir=[vx, vy, vz, focal_length])
p0
v0
p0
v0
focal_length
(negative)

## Slide 13: Photon detection and partial path lengths
MCX/MMC detectors are defined by a spherical shell intersect with the tissue boundary.
Detection only happens when a photon escape from “domain” to “background” (0-voxels or out-of-bounding-box in MCX)
For any detected photon: total pathlength L is a sum of the cumulative pathlength in each tissue type
= PPL1 + PPL2 + PPL3
User-customizable output (--savedetflag/-w ‘DSPMXVW’)
  D – output detector ID (detps.detid)
  S – partial-scattering event counts (detps.nscat)
  P – partial-pathlengths (detps.ppath)
  M – (partial) momentum transfer (detps.mom)
  X – exit photon positions (detps.p)
  V – exit photon directions (detps.v)
  W – initial packet weight (detps.w0)
tissue#1
tissue#2
tissue#3
src
det

## Slide 14: Knowing the limits
MCX website: http://mcx.space
MCX’24
Session 1.D

## Slide 15: Knowing the limits is the key
Avoid brute-force
  MC is slow in large voxel/mesh size, excessive time gates, large photon number - start with less demanding settings, move up only when results is not stable
Give MCX resources is the key to speed
  The more GPU cores, the faster speed. Giving MCX better hardware, it can scale linearly
Domain discretization matters
  Voxelated domain does not work well in transparent/low-scattering medium
Unjustified optical properties negate your accuracy gain
  A simulation is only as good as the chosen settings
Complexity is not always good
  You can make your simulation as realistic as possible, but at some point, increase in complexity yields diminished gain, know where to stop

## Slide 16: Hardware Recommendations
MCX website: http://mcx.space
MCX’22
Session 1.E

## Slide 17: Recommended Hardware
The more cores, the merrier! Use many consumer-grade cards together!
MCX (CUDA) is NVIDIA GPU only; MCXCL/MMCL can run on (almost) all processors. But CUDA is faster than OpenCL.
MCX uses single-precision floating-point operations, Tesla cards (more expensive) are not necessarily faster.
Dedicated GPU preferred – i.e. not used for display. Multiple-cards can gain speed almost linearly.
MCX
MCX-CL
MMC
Fiji, Polaris,Vega,
Navi

## Slide 18: GPU Benchmarks/Contest
http://mcx.space/gpubench

## Slide 19: MCX1